## Slide 1: Performing AC Analyses on PFC Converters
March 28, 2017
Chris Bridge
Tom Wilson
SIMPLIS Technologies

## Slide 2: Agenda
The Importance of Finding Steady-State
  Natural and Forced Response
  The State-Plane
POP/AC Analysis on PFC circuits
  AC Line vs. DC Line
  PFC: Continuous Conduction Mode
  PFC: Critical Conduction Mode
Multi-Tone AC Analysis
  PFC: Continuous Conduction Mode
  PFC: Critical Conduction Mode
Current Loop and Input and Output Impedance

## Slide 3: Agenda
The Importance of Finding Steady-State
  Natural and Forced Response
  The State-Plane
POP/AC Analysis on PFC circuits
  AC Line vs. DC Line
  PFC: Continuous Conduction Mode
  PFC: Critical Conduction Mode
Multi-Tone AC Analysis
  PFC: Continuous Conduction Mode
  PFC: Critical Conduction Mode
Current Loop and Input and Output Impedance

## Slide 4: The Importance of Finding Steady-State
A system must be operating in steady state in order to perform a valid AC analysis
Example: Series RLC with Natural and Forced Response
AC Response
OUT/IN
OUT
IN

## Slide 5: Multi-Tone AC Results Using different “Time Slices”
0 to 2 seconds
2 to 4 seconds
POP/AC
Not in Steady-State
Steady-State
15dB?

## Slide 6: Viewing PFC Performance in the State Plane
Recognize that the Dominant Energy Storage Elements are the Power Inductor and Output Capacitor
Define an X-Y Plot with the Inductor Current Plotted on y- Axis and the Output Capacitor Voltage on x-Axis
Time is now an Implicit Variable
Lowest Periodic System Behavior => ½ the Line Period

## Slide 7: Dominant Energy Storage Elements of PFC in State-Plane
Inductor Current
Output Voltage
State-Plane
1st Half-Cycle
2nd Half-Cycle
Output Voltage
Inductor Current

## Slide 8: Is This PFC Converter in Steady-State?
Inductor Current
Output Voltage
State-Plane
1st Half-Cycle
2nd Half-Cycle
Output Voltage
Inductor Current

## Slide 9: What Steady-State Looks Like on State-Plane
Inductor Current
Output Voltage
State-Plane
Output Voltage
Inductor Current

## Slide 10: Six Switching Cycles Around 10ms
Inductor Current
Output Voltage
State-Plane
Output Voltage
Inductor Current

## Slide 11: Six Switching Cycles Around 10ms
State-Plane
Output Voltage
Inductor Current

## Slide 12: State-Plane Progression

## Slide 13: Steady-State – AC Line
Inductor Current
Output Voltage
State-Plane
Output Voltage
Inductor Current

## Slide 14: Steady-State – AC Line, DC Line
State-Plane
Output Voltage
Inductor Current

## Slide 15: Summary of Methods for Finding Steady-State
AC Line:
  POP Analysis – Trigger on AC Line
  Long Transient – Use Multi-Tone AC Analysis
DC Line:
  POP Analysis – Trigger on Switching Frequency
  Long Transient – Use Multi-Tone AC Analysis

## Slide 16: Agenda
The Importance of Finding Steady-State
  Natural and Forced Response
  The State-Plane
POP/AC Analysis on PFC circuits
  AC Line vs. DC Line
  PFC: Continuous Conduction Mode
  PFC: Critical Conduction Mode
Multi-Tone AC Analysis
  PFC: Continuous Conduction Mode
  PFC: Critical Conduction Mode
Current Loop and Input and Output Impedance

## Slide 17: AC Line vs. DC Line
We will show that the AC analysis of a PFC Converter operating off a DC Line voltage is similar to the same converter operating from a AC Line.
DC Line Voltage is Set to the RMS Value of the AC Line
Why? Consider the state-plane:

## Slide 18: POP/AC Analysis on PFC circuits - Rules
AC Line
  Line Frequency Must be a Harmonic of the (constant) Switching Frequency
  Example: 50Hz line, and 100kHz Switching Frequency
  For AC Line with Variable Switching Frequency, use Multi-Tone AC Analysis
DC Line
  AC/DC Converter is Reduced to a DC/DC Converter
  Works on Converters with Constant or Variable Switching Frequency
  Extremely Fast when Compared to AC Line

## Slide 19: Continuous Conduction Mode PFC

## Slide 20: Continuous Conduction Mode PFC – POP/AC Results -- DC Line vs. AC Line
Voltage Loop:
DC Line
AC Line

## Slide 21: Critical Conduction Mode PFC

## Slide 22: Critical Conduction Mode PFC – POP/AC Results – DC Line
Voltage Loop:
DC Line

## Slide 23: Agenda
The Importance of Finding Steady-State
  Natural and Forced Response
  The State-Plane
POP/AC Analysis on PFC circuits
  AC Line vs. DC Line
  PFC: Continuous Conduction Mode
  PFC: Critical Conduction Mode
Multi-Tone AC Analysis
  PFC: Continuous Conduction Mode
  PFC: Critical Conduction Mode
Current Loop and Input and Output Impedance

## Slide 24: Multi-Tone Concept
Injection
Source
…
Inject multiple frequencies concurrently into a feedback loop during a time domain simulation
50 “tones” 1Hz ~ 50Hz
Post-process
w/ Fourier:
Loop Gain = Y/X
Phase
Gain
Y
X

## Slide 25: Continuous Conduction Mode PFC – POP/AC vs. Multi-Tone AC Results
Voltage Loop:
DC Line – POP/AC
AC Line – POP/AC
DC Line – Multi-Tone
AC Line – Multi-Tone

## Slide 26: Critical Conduction Mode PFC – Multi-Tone AC Results – DC Line, AC Line
Voltage Loop:
DC Line – POP/AC
DC Line – Multi-Tone
AC Line – Multi-Tone

## Slide 27: Agenda
The Importance of Finding Steady-State
  Natural and Forced Response
  The State-Plane
POP/AC Analysis on PFC circuits
  AC Line vs. DC Line
  PFC: Continuous Conduction Mode
  PFC: Critical Conduction Mode
Multi-Tone AC Analysis
  PFC: Continuous Conduction Mode
  PFC: Critical Conduction Mode
Current Loop and Input and Output Impedance

## Slide 28: Critical Conduction Mode: PFC Output Impedance
DC Line – POP/AC
AC Line – POP/AC

## Slide 29: Critical Conduction Mode: PFC Input Impedance
DC Line – POP/AC
AC Line – POP/AC

## Slide 30: Critical Conduction Mode: PFC Current Loop
DC Line – POP/AC
AC Line – POP/AC

## Slide 31: Simulation Time Comparison
Case | Input Voltage | CPU Time to Steady State | CPU Time for AC Analysis
AC Line, Multi-Tone AC | 115 VRMS AC | 238 sec | 304 sec
DC Line, Multi-Tone AC | 115 V DC | 240 sec | 322 sec
AC Line POP/AC | 115 VRMS AC | 76 sec | 88 sec
DC Line POP/AC | 115 V DC | 1 sec | 1 sec
Gain and Phase results are almost Identical, but…
Simulation times are very different !
If feasible, SIMPLIS POP and AC are much faster

## Slide 32: Summary
For PFC Voltage Loop and Zout
  DC Line input yields the same simulation results as the AC Line, but at a greatly reduced simulation time
  AC line results using POP/AC and Multi-Tone AC are nearly identical
PFC Current Loop response changes depending on AC Line vs. DC Line
  This impacts Zin

## Slide 33: Resources
Presentation:
  http://simplis.com/news/apec-2017
Webinar on this Topic:
  http://simplis.com/webinar/2016/11/17/ac-analysis-pfc
Training, Webinars:
  http://simplis.com/training

## Slide 34: “Companion Circuit” Technique: Compare Load Transient on 115VAC / 115VDC Input
DC Input
AC Input
We now have high confidence
our POP/AC results from the
“Companion Circuit” are valid
for the original, AC Input Circuit
But, we can always
run a Multi-Tone
AC Analysis

## Slide 35: Numerical Fourier Analysis:
Fundamental
Evaluate Fourier Integral at each Injected Frequency:
Injected Fundamental
Filter Gain
2nd Harmonic
Filter Gain
2nd, 3rd, 4th, ... harmonics rejected
Inter-harmonics are not perfectly rejected!
D:\customer.simplistechnologies.com\examples\internal\multi-tone\source_testing\filter_response_1.sxscr
1st, 3rd, 4th … harmonics rejected
Inter-harmonics are not perfectly rejected!
2nd harmonic
3rd Harmonic
Filter Gain
D:\customer.simplistechnologies.com\examples\internal\multi-tone\source_testing\filter_response_1.sxscr
1st, 2nd, 4th … harmonics rejected
Inter-harmonics are not perfectly rejected!
3rd harmonic

## Slide 36: Numerical Fourier Analysis: Observations
Filter selectivity increases with harmonic number
Increasing the # of fundamental cycles greatly increases filter selectivity
Injected Fundamental
↑ Fundamental to 3 Cycles
Filter rejects sub harmonics
and higher inter-harmonics

## Slide 37: Numerical Fourier Analysis: Observations
Low Frequencies will pass through into all data, but will be more prevalent in lower harmonics…
Therefore the circuit must be very well settled or the AC data will be corrupted!
9th Harmonic
1/10th Harmonic: only 20dB rejection
Increase in rejection to 38dB when n → 9